## Slide 1: FRAIG Functionally-Reduced And-Inverter Gate
B05901015 陳培威

## Slide 2: Balance between Sim & Fraig
Check the change of #fecgrp per simulation between intervals
INTERVAL | 100 | 100 | 100 | 1000 | 1000
CHANGE | 0.001 | 0.01 | 0.1 | 0.001 | 0.01
cirSim | 2.8 s | 7.5 s | 1.27 s | 7.5 s | 7.77 s
cirFraig | 53.95 s | 55.72 s | 54.58 s | 51.75 s | 52.66 s
total | 56.81 s | 57.08 s | 55.9 s | 59.3 s | 60.5 s
patterns | 19200 | 6400 | 6400 | 64000 | 64000
Less patterns but faster?
(will be discussed later)
Notes: 檢查區間內fecgrp改變的幅度
可以較快的讓random sim 停止
發現patterns數較少但總體時間較patterns多的快 報告最後討論

## Slide 3: Fraig
Observations
Algorithm
Some experiments & performances

## Slide 4: Fraig (Observations)
The more inputs, the longer it takes to prove
  Keep fanin cones minimized!!
    Ensure each proof is the simplest possible
  In an fecgrp, choose two bottom-most gates to prove!! (how?)
_DFSList!!
Notes: Fraig的時間看solver prove的時間
Proof 的時間看gate和input的數量
讓gate及input減少有助於減少proof 的時間
可以從最底層開始！_DFSList
希望讓每個待證明的fanin cones最小選擇最下面兩個gate
如何在一個fecgrp有效率找到這兩個gate?

## Slide 5
class CirGate
{
private:
… (gateID, lineNum, SimValue, _faninList, _fanoutList…)
size_t _pos; // position in _DFSList
}
class FecGrp
{
private:
IdList _data; // stored in literal ID e.g. 4 => 2, 5 => !2
unsigned _base; // gate with smallest _pos (closest to PIs)
}
Notes: _pos是gate在_DFSList的位置
_base是fecgrp中_pos最小的gate 也就是最先被遇到的

## Slide 6: Fraig (Algorithm)
・・・
1
2
3
4
・・・
・・・
・・・
・・・
5
Same fecgrp : 1 3 4 5
Base of group: 1
To ensure minimum fanin cones,
skip the base and merge others to it.
・・・
・・・
・・・
is base => skip
Nothing happens
Merge with 1
Merge with 1
Randomly choosing two gates may
involve unminimized fanin cones.
e.g. Choosing gate 1 & 5,
fanin cone of 5 is not minimized
Fanin cones are minimized in each proof!!
Notes: 假設…
隨機選取會導致fanin cone不是minimum
先跳過base 之後遇到同一組的再merge回去
強調：fanin cones會是最小的！！

## Slide 7: Fraig (Algorithm)
void cirMgr::fraig()
{
for g in _DFSList
if (!g->hasGrp() || g->isBase()) continue
base = g->base()
initSat(solver, base, g) // how often?
if (!solver.solve())
merge(g, base)
// where to continue fraiging?
else reSim(solver)
endFraig()
}
Notes: 要哪時候initialize solver？
Merge完要從哪裡繼續？

## Slide 8: Fraig (Experiments & performances)
When to initialize SAT solver?
PER PROOFS | 1 | 10 | 100 | 1000
cirSim | 1.27 s | 1.26 s | 1.27 s | 1.29 s
cirFraig | 54.58 s | 67.67 s | 68.30 s | 87.11 s
total | 55.90 s | 68.45 s | 69.20 s | 88.44 s
memory | 23.9 M | 48.1 M | 60.2 M | 82.3 M
Assign new vars every time
Assign vars once and add via DFS
Matters a lot!!
Notes: 每一次proof 完initialize 不僅時間上較有效率在記憶體使用上也是

## Slide 9: Fraig (Experiments & performances)
Where to begin after merging two gates?
  Fanin cone under the base is minimized
  Start from the base!!
Time | sim13.aag |  | sim12.aag | 
Starting from… | the base | the beginning | the base | the beginning
cirSim | 1.27 s | 1.25 s | 0.27 s | 0.28 s
cirFraig | 54.58 s | 56.11 s | 4.89 s | 4.79 s
total | 55.90 s | 57.42 s | 5.17 s | 5.08 s
Only matters a bit though…
Notes: 因為在base前的gate會先被iterate過所以應該是最簡的
所以可以從base開始！
但沒差很多

## Slide 10: Conclusion
No need to simulate too many patterns
  Fraig starts from the bottom, making it faster to disprove
  Resim takes less effort to divide than simulating
INTERVAL | 100 | 100 | 100 | 1000 | 1000
CHANGE | 0.001 | 0.01 | 0.1 | 0.001 | 0.01
cirSim | 2.8 s | 7.5 s | 1.27 s | 7.5 s | 7.77 s
cirFraig | 53.95 s | 55.72 s | 54.58 s | 51.75 s | 52.66 s
total | 56.81 s | 57.08 s | 55.9 s | 59.3 s | 60.5 s
patterns | 19200 | 6400 | 6400 | 64000 | 64000
Less patterns but faster?
Notes: 因為fraig是從最底部開始 disprove所利用的時間較少
可以較快的利用得到的序列resim使fecgrp分得更細
彌補simulation較少的缺點

## Slide 11: Thank you!! :)